## Slide 1: Management of production
Exercise: Production Capacity

## Slide 2: Introduction
Management dilemma - how much to produce?
What does the number of products depend on?
How can production be increased?

## Slide 3: Production size factors
market requirements (demand - customers / supply - competition)
own production possibilities and capabilities - finance, capacity, technology ...
possibilities of obtaining resources (inputs) on the market - raw materials ...
economic efficiency indicators - labor productivity

## Slide 4: Production capacity
It represents the maximum amound of products that a production unit (line, group ...) can produce in a defined period (year, month, day ...) in compliance with the defined conditions (number of shifts, technological and organizational conditions ...).
The total production capacity is directly connected to the
- length of the period and
- the performance
.....of the two basic factors - production equipment and human labor

## Slide 5: Factors affecting production capacity
technical base - depends on production equipments and its use
technical performance of the equipment
assortment and labor of products
staff qualifications and production experience
usable working time fund

## Slide 6: Determination of total production capacity
Calculation of the usable time fund standard
Calculation of the standard of human labor and production equipment
Determination of total capacity

## Slide 7: 1. Calculation of the usable time fund standard
UTF = NTF * T - PD
NTF = CTF - (Sa + Su + Ho)
UTF - usable time fund (usually in hours)  maximum time employees can work without breaks
NTF (working days) - nominal time fund (usually in days)
CTF - calendar time fund (in days for the relevant period)
T - number of work units in one day (number of changes * number of hours per shift)
PD - planned downtime in the given period
Sa, Su, Ho - Saturdays, Sundays, holidays

## Slide 8: 2. Standard of performance of human labor and production equipment
Standard of performance of human labor and production equipment: can take the form of a labor standard (time standard) or a performance standard (quantity)
labor standard (LS): the time required to perform a work operation
NP = Tm + Ta + RT
Tm = time of the main technological run  N of shifts * Hrs per shift
Ta = time of auxiliary (supporting) technological operation
RT = rest time (of machines)
performance standard (PS): the number of units that can be processed,
production per unit of time (inverse value of the labor standard) - depends on the product (shape, quality ...); requirements for packaging, logistics ...; the technical level of the production facility; work organization
PS = 1/LS
PS= 1/Tm + Ta + RT

## Slide 9: 3. Determination of total capacity
Tcap = UTF / LS
Tcap = UTF * PS
Tcap - total capacity
UTF – Usable time fund (usually in hours)
LS – Labor standard (usually in working days or minutes, hours)
PS - performance standard

## Slide 10: Example A – yogurt filling line
Calculation of the capacity of the yogurt filling line
The technical parameters of the line allow you to fill 50 quarter-liter yogurts per minute
The production technology always requires one production batch (filling volume 1250 L) to interrupt the operation for 15 minutes (cleaning and exchange of contents)
Rest time for the necessary manual activities is 0.5 min. for the handling batch
The carton (manipulative dose) contains 100 yoghurts
Production is two-shift (after 8 hours), it does not work on Saturdays or Sundays
Line maintenance is preventive and regular (always 15 minutes before the start of the first change - outside working hours) and 2 hours (within working hours) always once a month
Determine the production capacity of the line for the month of November (4 weekends and 1 holiday)

## Slide 11: The solution
1. The UTF for November (hours) shall be computed first
Length of one shift = 8 hours
CTF = 30 days
NTF = 30 - (4 * 2) - 1 = 21 working days
UTF = 21 * 2 * 8 = 336 h - 2 hours for maintenance = 334 h
4 weekends (S, N)
holiday
Number of shifts per day
Duration of one shift
UTF = NTF * T - PD
NTF = CTF - (Sa + Su + Ho)

## Slide 12
2. Calculation of the standard of time (labor) per one manipulative dose (100 pcs) and the standard of quantity per hour
Tm (min) = MD (pcs)/TC (pcs.min-1)
Time of the main technological run (course of the batch) .... 100/50 = 2min 2 min / 100 pcs (100 pcs is in one dose) ....1 dose = 50 pcs.min-1
Ta (min.pcs-1) = MA (min) / MA (pcs)
Auxiliary technical batch run time ... 15 / (4 * 1250 L) = 0,003 min.pcs-1 .....0.003* 100 (pcs per dose) = 0.3 min ... (0.3 min / 100pcs)
RT (min)
Rest time for manual operations ... 0.5 ... (0.5 min / 100 pcs)
LS = Tm + Ta + RT
Labor standard (time) per manipulative dose... 2 + 0.3 + 0.5 = 2.8 min .... (2.8 min / 100 pcs = 0.028 min.pc-1)
Labor standard (time) per batch 1250*4 pcs= 5000 (4 yog ¼l out of 1l)...0.028 min.pc-1 * 5000 pcs = 140 min(140 min / 5000 pcs)
PS = 1/LS
Performance standard (quantity in 1 hour).... 60 (min per hour) / 0.028 min.pc-1 = 2142.85 pcs.hour-1
alternative calculation....140 min/5000 pcs = ... (100 / 2,8) * 60 = 2143 .... (2143 pcs / hour)
MD – Manipulative dose (pcs)
TC – technological capacity pcs.min-1
MA- Maintenance (break time in min) or (loses in pcs)
LS = Tm + Ta + RT
Tm = time of the main technological run (min)
Ta = time of auxiliary technological operation (min)
RT = rest time

## Slide 13
3. Calculation of Tcap - Total capacity
Tcap = 334 * 2143 = 715 714 pcs of yogurts for November (maximum)
The maximum total capacity for November is 715 71 yogurts.
Production reality: It is necessary to proceed from the nature of the product (unused filling cannot remain in the line until the next day)
One wotking day = 2 shifts (2*8*60) = 960 min
Number of completed batches per day= in 2 shifts .... 960 (min)/140 (min.batch-1)= 6.86 = 6 batches
21 working days * 6 batches * 5000 pcs (1 batch) = 21 * 6 * 5000 = 630 000 pcs.month-1
The real total capacity for November is 630,000 yogurts.
Calculate the sales difference!
UTF
PS
Tcap = UTF / LS
Tcap = UTF * PS
Tcap - Total capacity
UTF – Usable time fund
LS – Labor standard
PS - Performance standard

## Slide 14: Example B – Beer filling line
Calculation of beer filling line capacity
The technical parameters of the line enable the filling of 900 half-liter beers per hour
Production technology always requires one production batch (filling volume 1500 L) to interrupt the operation for 20 minutes (cleaning and exchange of contents)
Rest time for the necessary manual activities is 0.6 min. for the handling batch
The carton (handling batch) contains 48 beers
Production is two-shift, it does not work on Saturdays or Sundays
Line maintenance is preventive and regular (always 15 minutes before the start of the first change – i.e. outside working hours) and 1.5 hours (within working hours) always once a month
Determine the production capacity of the line for the month of April (4 weekends and 2 holidays)

## Slide 15: The solution
UTF for April will be set first
Shift = 8 hours
CTF = 30 days
NTF = 30 - (4 * 2) - 2 = 20 working days
UTF = 20 days * 2 per day* 8 hours = 320 h - 1.5 hours maintenance = 318.5 hours
4 weekends (S, N)
holiday
Number of changes
Duration of one shift
UTF = NTF * T - PD
NTF = CTF - (Sa + Su + Ho)

## Slide 16
2. Calculation of the LS - standard of time (labor) per one manipulative dose(48 pcs) and the standard of quantity per hour
Tm - Time of the main technical course of the batch 48pcs/ (900pcs/hour = 900:60 = 15 pcs.min-1)= 3.2 min.....3.2 min / 48 pcs
Ta - Auxiliary technical batch run time (20min/ (2 beers/liter *1500 litres/batch)) * 48 pcs in dose = 20/(2*1500) =0.32 min ... (0.32 min/ 48pcs)
RT - Rest time for manual operations 0.6 min ... (0.6 min / 48 pcs)
LS - Labor standard (time) per manipulative dose ... 3.2 + 0.32 + 0.6 = 4.12 min ... (4.12 min / 48 pcs)
4.12 min / 48 pcs = 0.08583 min.pc-1
LS – Labor standard (time) per batch (1500 liters 2 beers/liter = 3000 pcs) ... 0.08583 min.pc-1* 3000pcs =257.5min = 257.5 min/3000pcs
Alternative calculation...4.12 * 3000/48 = 257.5 (257.5 min / 3000 pcs)
PS - Performance standard (quantity) per 1 hour ... (48 / 4,12) * 60 = 699 .... (699 pcs.hour-1)
LS = Tm + Ta + RT
Tm = time of the main technological run (min)
Ta = time of auxiliary technological operation (min)
RT = rest time
Tcap = UTF / LS
Tcap = UTF * PS
Tcap - Total capacity
UTF – Usable time fund
LS – Labor standard
PS - Performance standard
PS = 1/LS
PS= 1/Tm + Ta + RT

## Slide 17
3. Calculation of Tcap total capacity
Tcap = 318.5 * 699 = 222 641 pieces of beer for April (maximum)
The maximum total capacity for April is 222,641 beers.
Production reality: It is necessary to proceed from the nature of the product (unused filling cannot remain in the line until the next day)
UTF
PS
Tcap = UTF / LS
Tcap = UTF * PS
Tcap - Total capacity
UTF – Usable time fund
LS – Labor standard
PS - Performance standard
One wotking day = 2 shifts (2*8*60) = 960 min
Number of completed batches per day= in 2 shifts .... 960 (min)/257.5 (min.batch-1)= 3.73 = 3 batches
20 working days * 3 batches * 3000 pcs (1 batch) = 20 * 3 * 3000 = 180 000 pcs.month-1
The real total capacity for April is 180,000 yogurts.
Calculate the sales difference!

## Slide 18: Example C- Total annual capacity I.
The company produces 4,000 parts per hour. This year there are 114 days of weekends and holidays. Other time losses (holidays, illnesses, etc.) account for 35 days. The company is working on 2 shifts (each for 8 hours).
a) Calculate the total annual production capacity.
Tcap = UTF * PS
UTF (Usable time fund) = (365 - 114 - 35) * 8 * 2 = 3456 hours
PS (Performance standard) = 4000 pcs / hour
Tcap (Total capacity)= 13,824,000 pcs
b) Calculate the capacity utilization in the company (in%), if the company actually produced 12,985,000 pieces.
Capacity utilization = Real volume / Tcap = 12,985,000 / 13,824,000 = 93.9%

## Slide 19: Example D- Total annual capacity II.
The company produces 3,500 parts per hour. There are 113 days of weekends and holidays. Other time losses (holidays, illnesses, etc.) take 40 days. The company is working on 2 shifts (each for 8 hours).
a) Calculate the total annual production capacity.
Tcap (Usable time fund) = UTF * PS
UTF (Usable Time Fund) = (365 - 113 - 40) * 8 * 2 = 3392 h
PS (Performance Standard) = 3500 pcs / h
Tcap (Total capacity)= 11,872,000 pcs
b) Calculate the capacity utilization in the company (in%), if the company actually produced 10,782,000 pieces.
Capacity utilization = Real volume / Tcap = 10,782,000 / 11,872,000 = 90.8%

## Slide 20: Questions?.?